## Slide 1: Calibration Curves
1000 to 5000 ppm – Increments of 1000 ppm

## Slide 2: Calibration Curves
Fructose |  | Dextrose |  | Sucrose |  | Maltose |  | Malt3 |  | Malt4 | 
g/lit | Area | g/lit | Area | g/lit | Area | g/lit | Area | g/lit | Area | g/lit | Area
0.166 | 117692 | 0.166 | 116947 | 0.166 | 119224 | 0.167 | 117452 | 0.166 | 97311 | 0.166 | 82794
0.332 | 221335 | 0.332 | 225473 | 0.332 | 253286 | 0.333 | 232430 | 0.331 | 215132 | 0.331 | 117942
0.499 | 366497 | 0.499 | 377819 | 0.499 | 392675 | 0.500 | 384555 | 0.498 | 351185 | 0.498 | 184722
0.666 | 614121 | 0.666 | 599447 | 0.666 | 572268 | 0.667 | 603267 | 0.664 | 547480 | 0.664 | 287493
0.832 | 1026310 | 0.832 | 1013099 | 0.832 | 1052692 | 0.834 | 948029 | 0.829 | 838894 | 0.829 | 551339
0.0394 | 20594 | 0.0394 | 28556 | 0.0394 | 23021 | 1.5385 | 1043259 | 1.571 | 967334 | 0.0313 | 29536
0.042 | 28954 | 0.042 | 27657 | 0.042 | 28397 | 0.203 | 117498 | 0.042 | 38251 | 0.537 | 285817
0.357 | 187266 | 0.357 | 223393 | 0.357 | 200435 | 2.143 | 1296803 | 0.355 | 219133 | 0.378 | 175821
0.499 | 271685 | 0.500 | 333523 | 0.500 | 278922 | 0.499 | 313651 | 0.500 | 304513 | 0.500 | 238809
0.039 | 20594 | 0.039 | 27657 | 0.039 | 23021 | 0.167 | 117452 | 0.042 | 38251 | 0.031 | 29536
0.832 | 1026310 | 0.832 | 1013099 | 0.832 | 1052692 | 2.143 | 1296803 | 1.571 | 967334 | 0.829 | 551339

## Slide 3: Calibration Curves
Linear Fit
2nd Order Polynomial
Logarithmic Fit

## Slide 4: Calibration Curves
Concentration Curve Parameters |  |  |  |  |  | 
 | Fructose | Dextrose | Sucrose | Maltose | Malt-3 | Malt-4
Slope | 7.86E-07 | 8.21E-07 | 7.81E-07 | 1.43E-06 | 1.32E-06 | 1.49E-06
Y-int | 0.13 | 0.11 | 0.13 | -0.04 | 0.03 | 0.11
R2 | 0.87 | 0.90 | 0.86 | 0.89 | 0.89 | 0.87
a | -9.03E-13 | -8.49E-13 | -8.60E-13 | 1.16E-12 | 5.14E-13 | -2.66E-12
b | 1.71E-06 | 1.67E-06 | 1.68E-06 | -1.30E-07 | 7.91E-07 | 3.04E-06
c | 0.0141 | -0.0010 | 0.0057 | 0.2742 | 0.1068 | -0.0413
R2 | 0.97 | 0.99 | 0.97 | 0.94 | 0.90 | 0.96
Coef | 0.201 | 0.210 | 0.202 | 0.626 | 0.373 | 0.278
B | -2.048 | -2.170 | -2.073 | -7.315 | -4.121 | -2.903
R2 | 0.92 | 0.93 | 0.91 | 0.73 | 0.72 | 0.93

## Slide 5: Experimental Results (70 C @ 55 min)

## Slide 6: Extract vs. Time

## Slide 7: M-Sugars vs. Time

## Slide 8: M-Sugars vs. Time (Normalized

## Slide 9: Different Modeling Methods
1st Order Kinetic Principles
  System of ODE’s captures behavior
  Doesn’t predict sugars based on proposed reaction kinetics
Monte-Carlo Probability
  “Overkill”
Michaelis-Menten Enzyme Kinetics
  Based on Substrate and Enzyme Concentrations
Wort Carbohydrate Model @ 63°C

## Slide 10: Michaelis-Menten Enzyme Kinetics
General Reaction Rate:
E + S  E-S  E + P
E – Enzyme
S – Substrate
E-S – Enzyme-Substrate Complex
P - Product
k1
k-1
k2

## Slide 11: Notes On Board
Pause

## Slide 12: Proposed Hydrolysis Mechanism
Enzymes:
  β - Beta Amylase
  α - Alpha Amylase
Substrate:
  Starch
    AP - Amylopectin
    A - Amylose
Products:
  M1 - Mono-Saccharides (Fructose, Dextrose)
  M2 - Di-Saccharides (Sucrose, Maltose)
  M3 -Tri-Saccharides (Malto-Triose)
  M4 - Tetra-Saccharides (Malto-Tetraose)
  M>4 - Oligosaccharides (Higher Order Sugars)
  D - Dextrins
Eβ + AP  Eβ –AP  Eβ + M1 + M2 + D + M>4
Eβ + A  Eβ –A  Eβ + M1 + M2 + D + M>4
Eα + AP  Eα –AP  Eα + M1 + M2 + M3 + M4 + M>4 + D
Eα + A  Eα –A  Eα + M1 + M2 + M3 + M4 + M>4 + D

## Slide 13: Assumptions/Simplifications
Inability to distinguish between α and β Initial Concentrations:
  Eα + Eβ = E
Inability to distinguish between AP and A Starch
  Both Starches lead to same products
  AP + P = S
Dextrin Formation is negligible wrt Sugars’s
  dD/dt = 0
Starch hydrolysis is to completion
  No [A] or [AP] left over in products
  Ie: Everything is converted to Higher Order Sugars

## Slide 14: Simplified Model
 E + M2
 E + M3
 E + M4
k2
k3
k5
k4
E + S   E –S
kf
kb
 E + M1

r1= kf[E][S] - kb[ES]
r2= k2[ES]
r3= k3[ES]
r4= k4[ES]
r5= k5[ES]
rE= -r1 + r2 + r3 + r4 + r5+ r6
Reaction Rates:
Species Rates:
rS= -r1
rES= r1 - r2 - r3 - r4 - r5 - r6
rM1= r2
rM2= r3
rM3= r4
rM4= r5
 E + M>4
k6
r6= k6[ES]
rM>4= r6

## Slide 15: Simplified Model: Quasi-Steady State
QSS on formation of [ES] complex
  This reaction intermediate formation is negligible wrt other system rates
  d[ES]/dt = 0
  Plug in Rate Laws: Solve for E
Apply Enzyme Balance: [E] = [Eo] – [ES]
  Solve for [ES]
rES= 0 = r1 - r2 - r3 - r4 - r5 - r6
r1 = r2 + r3 + r4 + r5 + r6

## Slide 16: Solving
Where,

## Slide 17: Getting Km and Vmi
Hanes-Woolf Plot
  
  Plot vs [S]
    Slope = int =

## Slide 18: Experimental Hanes Wolf Plots